## Slide 1: SPCNVMe Introduction and Design
Roy Wang
a.k.a. SmokingPC

## Slide 2: TOC
NVMe Overview
Important Behavior and Sequence
Admin and I/O Queue
Command and Completion
SCSI Translation
Reference

## Slide 3: What is SPCNVMe ?
an OpenSource PCIe NVMe driver for Windows Platform
Implemented by Storport Miniport framework
Supported only Win 8+
  Maybe I will make it support Win7 when I have free time.... :p
Some information are reversed from windows built-in stornvme.sys.

## Slide 4: Overview

## Slide 5: Logical View of NVMe system
A NVMe device has controller and namespaces
  Actually NVMe support multiple controller but SpcNVMe doesn’t support it yet.
Each namespace has different format(e.g. block size)
Each namespace can represent one “Disk” in windows view.
PCIe
NVMe Device
Controller
Namespace(NS) 1
Namespace(NS) 2
...... NS 3~127

## Slide 6: Logical View of NVMe system
NVMe Device
Device Registers
Admin Queue Pair x1
I/O Queue Pairs xN
I/O Queue Pairs xN
I/O Queue Pairs xN

## Slide 7: Logical View of NVMe system
Terms Definition in spec
  Host : OS Layer which your driver running
  Device : Your NVMe device
Host control / communicate / submit commands to device, get completion and result from device.
Haradware Layer
NVME Device
Host
(OS Layer)

## Slide 8: Register Region and QueuePair
For NVMe device, there is one “Global” register region.
  Each PCI device has its own i/o address and register address. They are used to communicate with hardware to perform actions you want.
  By registers, you can enable(startup)/disable(shutdown) device, check status and other informations are done by registers.
Use QueuePair for communication
  Host submit commands to device via SubmissionQueue (SubQueue)
  Host retrieve command result from device via CompletionQueue (CplQueue)
  1 SubQueue + 1 CplQueue == 1 QueuePair

## Slide 9: QueuePairs
In device, 1 QueuePair for admin requests
  E.g. register I/O queue, identify controllers and namespaces, query SMART info, setup Interrupt Coalescing…etc.
Multiple I/O QueuePairs for I/O related requests
  Minimum 1 I/O QueuePair in each device, max depends on vendors
QueueSize is “How many entries a Queue has?”
  Host must register queue size before use them
  SubQ size can be different from CplQ size
  Of course, it’s better that set same size for them.

## Slide 10: Queue and Doorbell
NVMe Device
Submittion Queue
Completion Queue
Request
Response

## Slide 11: Queue and Doorbell

## Slide 12: Queue and Doorbell
Both SubQueue and CplQueue are implemented by ring buffer
  Producer / Consumer concept
  Doorbell / Interrupt notification
Host should “notify” device when sent new request into SubQueue, and “notify” device when retrieved(picked) results from CplQueue.
  Use Doorbells
Device should “notify” host when new result arrived to CplQueue.
  Use Interrupts

## Slide 13: Queue and Doorbell
Producer : Update index “Tail” and notify consumer
Consumer : Update index “Head” and notify producer
Doorbells are registers for corresponding queue that notify device something(head or tail) changed.
  In SubQ, Host should update doorbell to tell device “new SubQ Tail”
  In CplQ, Host should update doorbell to tell device “new CplQ Head”

## Slide 14: Admin Cmd and I/O Cmd
The NVMe command are defined as 2 group
  Admin command : set Interrupt Coalescing, register I/O queue…etc.
  I/O command : Read / Write / Verify …etc.

## Slide 15: Commands of NVMe system
Admin Commands
  Submit to admin queue
  I/O Queue Management(create / delete)
  Identify Controller and Namespace
  Get LogPage (e.g. SMART infor)
  Namespace Management
  Firmware Management
  Query / Set extra feature of controller
  ......etc.

## Slide 16: Commands of NVMe system
NVM Commands (I/O commands)
  Submit to I/O queue
  Read data
  Write data
  Copy and verify
  Flush
  Write Zero
  ......etc.

## Slide 20: Important Behavior and Sequence

## Slide 21
Init Controller
shutdown controller (SHN == 1)
reset controller
Queue Register/Unregister sequence

## Slide 22: Admin and I/O Queues

## Slide 24: NVMe Queue
NVMe Device
Submittion Queue
Completion Queue
Request
Response

## Slide 25: NVMe Queue Concept
All queues are kind of ring buffer structure with doorbell notification .
Submittion Queue
  Submit NVME_COMMAND to NVME device
  After submit, update doorbell to notification device
Completion Queue
  Retrieve command result from NVME device
  Device trigger interrupt back to driver for notification
1 SubQ + 1 CplQ  a QueuePair

## Slide 26: Ring Buffer concept
Producer / Consumer model
QHead and QTail ptr
  Producer updates QTail ptr (write)
  Consumer updates QHead ptr (read)
  If Head == Tail, queue is full.
    Stop pushing entries into queue.

## Slide 27: Ring Buffer concept

## Slide 28: NVMe Submittion Queue
Each command put into this queue by sequence
Using NVME_COMMAND structure as entry
SubQHead and SubQTail cursor
  Sender update SubQTail to indicate “where is latest submitted entry”
  NVMe device update SubQHead to indicate “where is latest consumed entry”

## Slide 29: How to transmit data with command
To transmit data with commands, sender have to prepare some physical pages to store data
  Sender should set PRP field to store these data
Host should prepare these pages to read from/write to NVMe device.
Physical Region Page (PRP)
Scatter Gather List (SGL)

## Slide 30: Admin Queue and I/O Queue
SubmitQueue
SubQ-0
SubQ-1
SubQ-2
SubQ-3
…
…
…
SubQ-N
CompletionQueue
CplQ-0
CplQ-1
CplQ-2
CplQ-3
…
…
…
CplQ-N
Admin Q
I/O Queue 1
I/O Queue 2
I/O Queue N

## Slide 31: Admin Queue and I/O Queue
Each QueuePair has 1 SubmitQueue and 1 CompletionQueue
Each NVMe device has 1 Admin QueuePair and N I/O QueuePairs.
  Admin QueuePair for admin command.
  I/O QueuePairs for I/O requests

## Slide 33: Command and Completion

## Slide 34: NVME Command
Total 64 Bytes, defined in nvme.h struct _NVME_COMMAND
  NVMe spec 1.3 Figure11
  CDW0 : 4 bytes
  NSID : 4 bytes
  MPTR : 8 bytes
  DPTR (PRP1 and PRP2) : 16 bytes
  CDW10 ~ CDW15 : 4 bytes for each

## Slide 35: NVME Command
OpCode、Fuse、PSDT、CID
Namespace ID
PRPs
Structures for corresponding command

## Slide 36: NVME Command – CDW0
Refer to NVMe 1.3 Figure 10
  OpCode : cmd code. Admin and I/O command has different OpCode
    E.g. NVME_ADMIN_COMMAND_IDENTIFY == 6
  FUSE : fused operation
  CID : command id, should be unique in entire device currently processing
  PSDT : select DPTR or MPTR to transfer data. Default 00 == DPTR (use PRP)

## Slide 37: NVME Command – NSID
Refer to NVMe 1.3 Figure 11
  Select Namespace ID that this command applies to.
  1-based index id
  If cmd doesn’t need NSID, set this field to 0
  If apply this command to all namespaces, set this field to 0xFFFFFFFF
  Wrong NSID will cause cmd failed.

## Slide 38: NVME Command – MPTR and DPTR
Refer to NVMe 1.3 Figure 11
  MPTR is reserved for NVMe over Fabric (so I didn’t use)
  DPTR is common way to pass data buffer with NVMe command.
    I only use PRP, not SGL.
  PRP contains PhysicalAddress of data buffer.

## Slide 39: NVME Command – PRP (DPTR) rules
In all condition, PRP1 should be DWORD aligned at least. PRP2 should be page aligned.
All following address means “PhysicalAddress”
  If buffer doesn’t across page boundary, PRP1 == address of buffer start, and PRP2 == 0
  If buffer across one page boundary, PRP1 == address of buffer start, and PRP2 == next page start address
    E.g. buffer va=0xffff80a000001730, pa = 0x0000000005942730 length 0xC00. PRP1 == 0x0000000005942730 and PRP2 == 0x0000000005943000

## Slide 40: NVME Command – PRP (DPTR) rules
  If buffer across 2 or more page boundary, PRP1 is buffer start address, PRP2 is another allocated new PAGE(1 page only). In this page stores address array of following buffer address.
    E.g. assum a buffer va=0xffff80a000001730, pa=0x0000000005942730, length=0x1A00.
    PRP1 == 0x0000000005942730, PRP2 == another page (assume it is 0x0000000006007000, named PHYSICAL_ADDRESS *prp2_list pointer points to this page).
    prp2_list[0]==0x0000000005943000, prp2_list[1]== 0x0000000005944000

## Slide 41: NVME Command –

## Slide 42: NVME Command –

## Slide 43: SCSI Command Translation

## Slide 44: SCSI Translation

## Slide 46: Reference
NVMe 1.3 spec
  https://nvmexpress.org/wp-content/uploads/NVM_Express_Revision_1.3.pdf
Windows StorNVMe driver SCSI Translation Support
  https://github.com/MicrosoftDocs/windows-driver-docs/blob/staging/windows-driver-docs-pr/storage/stornvme-scsi-translation-support.md

## Slide 48: Appendix

## Slide 49: History of SSD
http://www.ssdfans.com/?p=8076
https://zh.m.wikipedia.org/zh-hant/NVM_Express