## Slide 1: SPCNVMe Introduction and NVMe Pricinples
Roy Wang
a.k.a. SmokingPC

## Slide 2: TOC
NVMe Overview
Important Behavior and Sequence
Admin Queue and I/O Queues
Command and Completion
Command Translation
Appendix

## Slide 3: What is SPCNVMe ?
an OpenSource PCIe NVMe driver for Windows Platform
Implemented by Storport Miniport framework
Supported only Win 8+
  Maybe I will make it support Win7 when I have free time.... :p
Some information are assembly reversed from windows built-in stornvme.sys.

## Slide 4: What can SPCNVMe do?
I implemented this driver with :
  Normal storage features
  Firmware download, query, and activate (planned in future)
  SED(self encrypted disk) cmds
  Windows storage system cmds

## Slide 5: Overview and Concept

## Slide 6: Logical View of NVMe system
A NVMe device has controller and namespaces
  Actually NVMe support multiple controller but SpcNVMe doesn’t support it yet.
Each namespace has different format(e.g. block size)
Each namespace can represent one “Disk” in windows view.
PCIe
NVMe Device
Namespace(NS) 1
Namespace(NS) 2
...... NS 3~127

## Slide 7: Logical View of NVMe system
NVMe Device
Device Registers
Admin Queue Pair x1
I/O Queue Pairs xN
I/O Queue Pairs xN
I/O Queue Pairs xN

## Slide 8: Logical View of NVMe system
Terms Definition in spec
  Host : OS Layer which your driver running
  Device : Your NVMe device
Host control / communicate / submit commands to device, get completion and result from device.
Haradware Layer
NVME Device
Host
(OS Layer)

## Slide 9: Communication Model and QueuePairs
NVMe Device
Submittion Queue
Completion Queue
Request
Response
Implememnted by RingBuffer, no locks
Notify “new cmd arrived”
Ack “completion received”
Notify “new completion arrived”

## Slide 10: Communication Model and QueuePairs
There is NO lock can be used between Host and Device.
Memory of Queues are share memory between Host and Device.
For share memory locking, NVMe implements these Queues as RingBuffer.
There are 2 types of Queue :
  Submittion Queue : Host sends commands to Device.
    struct NVME_COMMAND array
  Completion Queue : Device return the cmd result back to Host.
    struct NVME_COMPLETION_ENTRY array
  1 SubQueue + 1 CplQueue == 1 QueuePair

## Slide 11: Communication Model and QueuePairs
Each NVMe device has one (and only one) Admin QueuePair.
To do I/O on NVMe, there should be one I/O QueuePair at least.
  Spec defines max I/O queue is 65536
  Actual supported max I/O queue depends on vendor design.
Some device requires SubQ and CplQ of same QueuePair using continuous physical memory
  So in SpcNVMe, I always allocate them on continuous physical pages.

## Slide 12: Communication Model and QueuePairs
QueueSize is “How many entries a Queue has?”
  Host must register queue size before use them
  SubQ size can be different from CplQ size. Of course, better to set same size.

## Slide 13: Register Region
Use QueuePair for communication
  Host submit commands to device via SubmissionQueue (SubQueue)
  Host retrieve command result from device via CompletionQueue (CplQueue)
  1 SubQueue + 1 CplQueue == 1 QueuePair

## Slide 14: PCIe Device BAR0
NVMe device is like other PCI/PCIe devices, there is Bar0 to be mapped during StartupDevice
  StorPortGetBusData() can get PCI_COMMON_CONFIG data buffer.
  Storport will do it and parse this buffer BEFORE HwFindAdapter
    HwFindAdapter() pass it to miniport in PPORT_CONFIGURATION_INFORMATION:: AccessRanges
    NVMe CtrlRegister region comes from BAR0 in this parsing result.
    Doorbells page address is CtrlRegister+0x1000
    BAR0 is usually 4 PAGES long.
    DO NOT touch CtrlRegister+0x2000 and CtrlRegister+0x3000, unless you know what you’re doing. Corruption on that two pages will cause MSIX interrupt failure.

## Slide 15: PCIe Device BAR0
CtrlRegister
(1 PAGE)
Doorbells
(1 PAGE)
MSIX Table or MSIX-PBA Table
(1 PAGE)
MSIX Table or MSIX-PBA Table
(1 PAGE)
BAR-0 Space
(4 PAGES)
MSIX and MSIX-PBA tables’ sequence depend on device.

## Slide 16: NVMe CtrlRegister Region
For NVMe device, there is one “Global” register region.
  struct _NVME_CONTROLLER_REGISTERS in nvme.h
  enable / disable nvme device
  check status
  setup and register Admin QueuePair
  NVMe capability and version information
  ……etc.

## Slide 17: Doorbell and Interrupt
How does Host tell Device “new command arrived?”
  Host should update corresponding “SubQ Doorbell”.
How does Device tell Host “new completion result returned??”
How does Host tell Device “Host popped some results”
  Device use Interrupt to notify Host.
  Host use “CplQ Doorbell” to notify device.
SubQ and CplQ are RingBuffer implemented, no lock can be used. So it’s necessary to notify each others, to prevent ring overflow and underflow.

## Slide 18: Doorbell and Interrupt
SubQ and CplQ are implemented by RinBuffer
  Producer and Consumer I/O model
  Producer : Update index “Tail” and notify consumer
  Consumer : Update index “Head” and notify producer
In Cmd Submit, Host is Producer and Device is Consumer.
In Completion, Device is Producer and Host is Consumer.
Doorbells are registers for corresponding queue that notify device something(head or tail) changed.
  In SubQ, Host should update doorbell to tell device “new SubQ Tail”
  In CplQ, Host should update doorbell to tell device “new CplQ Head”

## Slide 19: Important Behaviors

## Slide 20: Init (Startup) NVMe Device
Init PCI/PCIe bus resources
Disable device controller
Setup Admin QueuePair
Enable controller
Setup necessary configs
Identify Controllers
Identify Namespaces
Set Features
Register I/O QueuePairs

## Slide 21: Shutdown Device
Set register to notify shutdown
Wait complete
Release Host resources
Disable controller

## Slide 22: Disable Device
Set register to disable controller
Wait complete

## Slide 23: Reset Device
Disable Device
Init Device

## Slide 24: I/O Queue Register
Register CplQ[n] first
then Register SubQ[n]
Loop until all desired QueuePairs has been registered.

## Slide 25: Identify Namespaces
NVMe 1.3 and 1.0 are different in this behavior
Query all active namespaces
Iterate returned namespace ids
Query each namespace information by adm cmd

## Slide 26: Identify Namespaces
VMWare simulated virtual nvme device only support NVMe v1.0 spec.
  NVMe v1.0 doesn’t support “Query All Active Namespace” command.
  Only query Namespace ID 1

## Slide 27: Set Features (NVMe spec 1.3)
You can skip SetFeatures step if you want it be default.
“MustHave” in Spec (“Mandatory” in SetFeature section)
  Arbitration (Round Robin weight of queue processing)
  Power Management (How to handle different power state)
  Temperature Threshold (Temperature upper/lower limit)
  Error Recovery
  Number of Queues (ask how many I/O Queues can be registered)
  Write Atomicity Normal
  Asynchronous Event Configuration (AsyncEvent will tell you what’s wrong)

## Slide 28: Set Features (NVMe spec 1.3)
Minimal Implementation
  Number of Queues
    Host tell Device “how many I/O queues I would like to register” and Device will reply “How many I/O queues MAX I can allow your registration”.
    This must be implemented! Not every device has 64 queues…
My Recommended Implementation
  Asynchronous Event Configuration
    It will reply event data if anything wrong. Replied event carries debug information.

## Slide 29: Register I/O Queues
Admin Command
  Create I/O Submission Queue
  Create I/O Completion Queue
Assign Physical Memory Address of QueueBuffer to PRP
In each QueuePair , always create Completion Queue before Submission Queue !
  Device will reject cmd if create SubQ before CplQ

## Slide 30: Queue Buffer Contiguous
In CtrlRegister->Cap , CQR field indicates “Registered Queue Buffer should be Physically Contiguous”
  Example : register a SubQ with 128 entries, the buffer must be 2 PAGE physically contiguous memory if CAP.CRQ == 1.
  SubQ no need to be contiguous with CplQ

## Slide 31: Admin Queue and I/O Queues
Communication with NVMe Device

## Slide 32: NVMe Queue
NVMe Device
Submittion Queue
Completion Queue
Request
Response

## Slide 33: NVMe Queue Concept
All queues are kind of ring buffer structure with doorbell notification .
Submittion Queue
  Submit NVME_COMMAND to NVME device
  After submit, update doorbell to notification device
Completion Queue
  Retrieve command result from NVME device
  Device trigger interrupt back to driver for notification
1 SubQ + 1 CplQ  a QueuePair

## Slide 34: Ring Buffer concept
Producer / Consumer model
QHead and QTail ptr
  Producer updates QTail ptr (write)
  Consumer updates QHead ptr (read)
  If Head == Tail, queue is full.
    Stop pushing entries into queue.

## Slide 35: Ring Buffer concept

## Slide 36: NVMe Submittion Queue
Each command put into this queue by sequence
Using NVME_COMMAND structure as entry
SubQHead and SubQTail cursor
  Sender update SubQTail to indicate “where is latest submitted entry”
  NVMe device update SubQHead to indicate “where is latest consumed entry”.
  SubQHead comes from CplQ Entry
    Each CplQ entry tells Host “when this completion go back, where is latest consumed NVME_COMMAND entry in device”.

## Slide 37: How to transmit data with command
To transmit data with commands, sender have to prepare some physical pages to store data
  Sender should set PRP field to store these data
  You can treat it as “buffer of command”, like calling API.
Host should prepare these pages to read from/write to NVMe device.
Physical Region Page (PRP)
Scatter Gather List (SGL)
  SpcNVMe doesn’t use this way.

## Slide 38: Admin Queue and I/O Queue
SubmitQueue
SubQ-0
SubQ-1
SubQ-2
SubQ-3
…
…
…
SubQ-N
CompletionQueue
CplQ-0
CplQ-1
CplQ-2
CplQ-3
…
…
…
CplQ-N
Admin QueuePair
I/O QueuePair 1
I/O QueuePair 2
I/O QueuePair N

## Slide 39: Admin Queue and I/O Queue
Each QueuePair has 1 SubmitQueue and 1 CompletionQueue
Each NVMe device has 1 Admin QueuePair and N I/O QueuePairs.
  Admin QueuePair for admin command.
  I/O QueuePairs for I/O requests
    Count of I/O QueuePairs depends on device
In implementation, it’s usually treat AdminQpair as QueuePair-0, I/O QPair as QueuePair-1 ~ QueuePair-N

## Slide 40: Command and Completion

## Slide 41: NVME Command
Total 64 Bytes, defined in nvme.h struct _NVME_COMMAND
  NVMe spec 1.3 Figure11
  CDW0 : 4 bytes
  NSID : 4 bytes
  MPTR : 8 bytes
  DPTR (PRP1 and PRP2) : 16 bytes
  CDW10 ~ CDW15 : 4 bytes for each

## Slide 42: NVME Command
OpCode、Fuse、PSDT、CID
Namespace ID
PRPs
Structures for corresponding command

## Slide 43: NVME Command – CDW0
Refer to NVMe 1.3 Figure 10
  OpCode : cmd code. Admin and I/O command has different OpCode
    E.g. NVME_ADMIN_COMMAND_IDENTIFY == 6
  FUSE : fused operation
  CID : command id, should be unique in entire device currently processing
  PSDT : select DPTR or MPTR to transfer data. Default 00 == DPTR (use PRP)

## Slide 44: NVME Command – NSID
Refer to NVMe 1.3 Figure 11
  Select Namespace ID that this command applies to.
  1-based index id
  If cmd doesn’t need NSID, set this field to 0
  If apply this command to all namespaces, set this field to 0xFFFFFFFF
  Wrong NSID will cause cmd failed.

## Slide 45: NVME Command – MPTR and DPTR
Refer to NVMe 1.3 Figure 11
  MPTR is reserved for NVMe over Fabric (so I didn’t use)
  DPTR is common way to pass data buffer with NVMe command.
    I only use PRP, no SGL.
  PRP contains PhysicalAddress of data buffer.

## Slide 46: NVME Command – PRP (DPTR) rules
VA = 0xffff80a000001730
Length = 0xC00
1st Page PA = 0x0000000005942730
2nd Page PA = 0x0000000005943000
PRP1 = 0x0000000005942730
PRP2 = 0x0000000005943000

## Slide 47: NVME Command – PRP (DPTR) rules
In all condition, PRP1 should be DWORD aligned at least. PRP2 should be page aligned.
All following address means “PhysicalAddress”
  If buffer doesn’t across page boundary, PRP1 == address of buffer start, and PRP2 == 0
  If buffer across one page boundary, PRP1 == address of buffer start, and PRP2 == next page start address
    E.g. buffer va= 0xffff80a000001730, pa = 0x0000000005942730 length 0xC00. PRP1 == 0x0000000005942730 and PRP2 == 0x0000000005943000

## Slide 48: NVME Command – PRP (DPTR) rules
VA = 0xffff80a000001730
Length = 0x1A00
1st Page PA = 0x0000000005942730
2nd Page PA = 0x0000000005943000
PRP1 = 0x0000000005942730
PRP2 = 0x0000000006007000
3rd Page PA = 0x0000000005944000
[Content of PRP2 page]
PHYSICAL_ADDRESS array
0x0000000005943000
0x0000000005944000

## Slide 49: NVME Command – PRP (DPTR) rules
  If buffer across 2 or more page boundary, PRP1 is buffer start address, PRP2 is another allocated new PAGE(1 page only). In this page stores address array of following buffer address.
    assum a buffer va=0xffff80a000001730, pa=0x0000000005942730, length=0x1A00.
    PRP1 == 0x0000000005942730
    PRP2 == another page allocated by Host (assume it is 0x0000000006007000, named PHYSICAL_ADDRESS *prp2_list pointer points to this page).
    prp2_list[0]==0x0000000005943000, prp2_list[1]== 0x0000000005944000
    The page of PHYSICAL_ADDRESS array can be only 1 PAGE long. Unsed elements should be filled by 0 to avoid unexpected issue.

## Slide 50: Windows Command Translation

## Slide 51: Cmd Translation?
In windows I/O model, storage system are managed and accessed by several different group of commands
  SCSI cmd for most requsts
  SCSI miniport cmd for Firmware related requests
  Storage property cmd for control and telemetry logging
Some SCSI commands are abandoned in Windows.
  No need to implement all SCSI command

## Slide 52: SCSI Translation Table (Admin Cmd)
SCSI Command | NVMe Command
Format Unit/Sanitize | (Adm) Format NVM
Inquiry | (Adm) Identify
Log Sense | (Adm) Get Features, Get Log Page
Mode Sense (10) | (Adm) Identify, Get Features
Read Capacity | (Adm) Identify
Read Data Buffer(16) | (Adm) Get Log Page
Report LUNs | (Adm) Identify
Security Protocol In / Security Protocol Out | (Adm) Security Receive / Security Send
Start / Stop Unit | (Adm) Set Features, Get Features

## Slide 53: SCSI Translation Table (I/O Cmd)
SCSI Command | NVMe Command
Read | Read
Write | Write
Verify | Verify
Synchronize Cache (10) | Flush
Unmap | Dataset Management

## Slide 54: Firmware Commands
Miniport IOCTL Command | NVMe Command
FIRMWARE_FUNCTION_GET_INFO (Firmware Query) | Get Log Page
FIRMWARE_FUNCTION_DOWNLOAD (Firmware Download) | Firmware Image Download
FIRMWARE_FUNCTION_ACTIVATE (Firmware Active) | Firmware Commit (Firmware Active in NVMe v1.0)

## Slide 55: Firmware Command Translation
Firmware related feature are implemented by SRB_IO_CONTROL structure and IOCTL_SCSI_MINIPORT_FIRMWARE command
  Cmd target to disk device, disk.sys forward it to NVMe driver
Another way to implement Firmware related feature is SCSI command WRITE BUFFER
  Cmd also target to disk device, and disk.sys also forward it to NVMe driver.
Microsoft recommended way is IOCTL_SCSI_MINIPORT_FIRMWARE

## Slide 56: Appendix

## Slide 57: About Index and ID
In Spec, You should mention about Index and ID number base
  Global QueuePair ID is 0-Based number.
    Admin QueuePair treat as QueuePair [0]
    I/O QueuePair ID is 1-based. It’s because Admin QueuePair exist.
      I/O QueuePair 1 == QueuePair[1], I/O QueuePair 2 == QueuePair[2]……and so on
  Controller ID : 0-Based index number
  NameSpace ID : 1-Based index number
    0 is INVALID_NAMESPACE_ID
    0xFFFFFFFF is NOT_SPECIFIC_NSID
In Read/Write cmds, LBA are 0-based
  How do you put “256” into 8bit? 0 is meaningless for such command.

## Slide 58: About “Number of XXX”
QueueSize of Admin QueuePair and I/O QueuePair
  ASQS and ACQS in struct NVME_ADMIN_QUEUE_ATTRIBUTES
  QSIZE in register i/o queue cmd.
  all of them are 0-Based number
NLB of Read/Write cmd : 0-Based number
Why 0-Based? Same as Read/Write cmd’s LBA

## Slide 59: Reference
NVMe 1.3 spec
  https://nvmexpress.org/wp-content/uploads/NVM_Express_Revision_1.3.pdf
Windows StorNVMe driver SCSI Translation Support
  https://github.com/MicrosoftDocs/windows-driver-docs/blob/staging/windows-driver-docs-pr/storage/stornvme-scsi-translation-support.md

## Slide 60: Reference
History of SSD
  http://www.ssdfans.com/?p=8076
  https://zh.m.wikipedia.org/zh-hant/NVM_Express